## Slide 1: MIMO Receiver Architecture
Wireless testcase
  Resistors, capacitors, transistors
  No inductors
  1-3 GHz operating frequency
  Clock distribution network as digital block

## Slide 2: MIMO Receiver Architecture
Wireless testcase
  Resistors, capacitors, transistors
  No inductors
  1-3 GHz operating frequency
  Clock distribution network as digital block
Main blocks
  Spectral filter
  Spatial filter (shown in green box)
  Transimpedance amplifier (shown in blue box)
  Clock distribution network

## Slide 3: TIA Layout
Manual Layout
ALIGN Layout
41.68μm × 48.585μm = 2025.02μm2
46.355μm × 48.18μm = 2233.38μm2
Schematic
Notes: In the presentation, point out the use of wide metal wires

## Slide 4: TIA Performance Verification
Parameters | Schematic | Manual Layout | ALIGN Layout
Open Loop Gain (dB) | 25.25 | 24.95 | 23.26
OL 3dB Frequency (MHz) | 160 | 157.8 | 181.1
Closed Loop Gain (dB) | 18.49 | 18.34 | 17.58
CL 3dB Frequency (MHz) | 87.43 | 85.71 | 91.86
Test Setup
RB and RF were schematic models for simulation

## Slide 5: Spectral Filter Layout
CA
c7
c8
c9
c10
c3
c4
c5
c6
Manual Layout
ALIGN Layout
Schematic
273.6μm × 420μm = 114912μm2
213.05μm × 441.56μm = 94074.36μm2
Notes: I have used the rotated version here – moved the CA annotation to the ALIGN layout since it comes first. Please explain You could talk about the constraint orally during the presentation

## Slide 6: Mixer-First RX
Transimpedance
Amplifier (TIA)

## Slide 7: MIMO v/s Mixer First
Spectral Filter
TIA
MIMO RX
Mixer-First RX

## Slide 8: Top-Level Layout of Mixer-First RX
189,841 μm2
132,901 μm2
Manual Layout
ALIGN Layout
Schematic

## Slide 9: Top Level Performance Verification: Mixer-first RX
ALIGN Layout results consists PEX results using individual layout of bottom plate mixer and TIA
Parameters | Schematic | Manual Layout | ALIGN Layout
Input Matching S11 (dB) | -15.79 @ 960 MHz | -14.27 @ 960 MHz | -10.9 @ 960 MHz
Best S11 (dB) | -15.79 @ 960 MHz | -19.17 @ 940 MHz | -17.35 @ 920 MHz
IF Bandwidth (MHz) | 118.5 | 107.78 | 114.45
Power Gain S21 (dB) | 18.12 | 15.22 | 15.23
NF (dB) | 8.21 | 11.94 | 11.51
Simulated at LO frequency of 1 GHz

## Slide 10: Spatial Filter Layout
Schematic
Manual Layout
ALIGN Layout
145.6μm × 284μm = 41350.4μm2
156.94μm × 309.47μm = 48568.22μm2

## Slide 11: MIMO Layout
Schematic
Manual Layout

## Slide 12: MIMO Layout
Manual Layout
Spectral filter hierarchy
Spatial beamformer hierarchy

## Slide 13: MIMO Sub-Hierarchy: Spatial Beamformers
Spatial beamformer block contains
  8 Spatial filters
  2 CLK driver buffers (used as black box input)
  1 I/O CLK distribution block (used as black box input)
Spatial filter
I/O CLK Distribution Block
CLK Drivers
Manual Layout

## Slide 14: MIMO Sub-Hierarchy: Spatial Beamformers
ALIGN Layout 1
Manual Layout

## Slide 15: MIMO Sub-Hierarchy: Spatial Beamformers
ALIGN Layout 2
Manual Layout

## Slide 16: TIA Layout
Manual Layout
ALIGN Layout
41.68μm × 48.585μm = 2025.02μm2
46.355μm × 48.18μm = 2233.38μm2
Schematic
Notes: In the presentation, point out the use of wide metal wires

## Slide 17: TIA Layout with new P&R
Manual Layout
ALIGN Layout
39.98μm × 45.715μm = 1827.68μm2
46.355μm × 48.18μm = 2233.38μm2
Schematic
Notes: In the presentation, point out the use of wide metal wires

## Slide 18: Update 02/07/2022
Mixer First RX
Placement looks symmetric and good for performance
Few wire shorts observed
LVS not clean
Ports have shorted